## Slide 1: CS118: Computer Network Fundamentals Lecture-1: introduction

## Slide 2: CS118: explains (roughly) how the Internet works
Internet: a huge, complex network of networks
Divide-and-conquer
  Figure out how many major parts,
  Learn one piece at a time
Your job:
  Read textbook, think, collect a list of questions
    review every lecture slide deck after each class
  Ask questions in class/office hours/via Piazza
  Practice what you learn through homework and projects

## Slide 4: Course assignment and due schedule
Midterm | In-class, Wednesday Feb 5 (Location TBD)
Final | 3:00PM-6:00PM Saturday March 21 (Location TBD)
Homework | Release: on Thursday of week 1, 3, 5, 7; Due: 11:59pm Tuesday of week 3, 5, 7, 9.
Project 0 | Release: Monday Jan 6, 2024 (Week 1) Due: 11:59pm Wednesday, Jan 15, 2024 (Week 2)
Project 1 | Release: Thursday Jan 16, 2024 (Week 2) Due: 11:59pm Sunday, Feb 16, 2024 (Week 6) Grading: auto-grading script (sample tests will be provided to let everyone test their code before submission)
Project 2 | Release: Monday, Feb 17, 2024 (Week 7) Due: 11:59pm Sunday, March 16, 2024 (Week 10) Grading: auto-grading script (sample tests will be provided to let everyone test their code before submission)
For all other course info, please see https://bruinlearn.ucla.edu/
1.5 weeks
4.5 weeks
4 weeks

## Slide 5: Course workload and grading
Bi-weekly homework assignments
3 programming projects,
  0. UDP socket (individual)
  1. Reliable data delivery (2-3 people team)
  2. Secured reliable data delivery (2-3 people team)
Midterm and final exams (cheat sheets allowed, 2 pages double sided)
Strict Grading Policy
  Homework: do it yourself; no credit for late submission
  Project: 20% credit reduction per late day
  No make-up exam
Homework | 20%
Programming Projects | 25% (5/ 10/ 10)
Midterm | 25%
Final exam | 30%
2% extra credits based on piazza
1% extra credits course evaluation and TA/LA feedbacks
Notes: Whether allow cheat sheer

## Slide 6: Class Policy
The following actions are strictly prohibited
Posting/sharing/selling class material, with or without answers, to anyone outside this class, during or after this quarter.
Use of old homework/midterm/finals in doing homework or exams
Use ChatGPT in doing assignments
Making your project code publicly available either during or after this quarter
  you must use private repository on GitHub or GitLab
Notes: plagiarism You can learn a lot from your classmates here at UCLA, so I strongly encourage you to try to get to know one another. The time before class starts is a great opportunity to talk with other students. Our cellphones can be very distracting, and often prevent us from getting to know people. Accordingly, as soon as you enter this room, please turn off your cellphone and put it away. This room should be a cell-phone free zone. If you really need to use your phone before class, please step out of the room and use it outside. I think you will find spending time away from your phone, and with the actual people around you, to be very worthwhile.

## Slide 7: Hints for Getting Good Grade
Review previous lecture slides
Read textbook before coming to each lecture
Ask questions
Get your work done early
  Lecture slides uploaded to BruinLearn one day before the lecture
  Get HWs and projects done before the deadline
Notes: have Thu lecture uploaded tonight

## Slide 8: Let’s get started Today we cover the basic concepts in Chapter 1 of the textbook

## Slide 9: What is a Computer Network
Internet
Notes: Can end user devices talk to each other directly? What if one does skype

## Slide 10: What is a Computer Network
Notes: This is a rather traditional picture, not the latest greatest

## Slide 11
Coming to you ....

## Slide 12: Terminology
billions of connected computing devices:
  hosts = end systems
  running network apps
  Apps send/receive data packets
communication links
  fiber, copper, radio, satellite
  transmission rate = bandwidth (BW)
wired
links
wireless
links
Routers = packet switches inside network
router
mobile network
global Internet
Service Provider
(ISP)
regional ISP
home
network
institutional
network
smartphone
PC
server
wireless
laptop
Recent years witnessed rapid growth of giant cloud service providers
Notes: 12

## Slide 13: “Nuts and Bolts”
Internet: “network of networks”
  Interconnected ISPs, enterprise networks, now also cloud service providers
Protocols: define how to send, receive packets
  e.g., HTTP, TCP, IP, 802.11
Internet protocol standards
  RFCs: “Request for Comments”
    https://www.rfc-editor.org/rfc-index.html
    Developed by Internet Engineering Task Force (IETF)
  IEEE Standards
  W3C (World Wide Web Consortium), and others
mobile network
global ISP
regional ISP
home
network
institutional
network

## Slide 14: What is a protocol?
… specific messages sent
… specific actions taken when the messages received
human protocols:
Traffic light protocol
Green: go
Red: stop
Yellow: slow down - stop
Hi
Hi
Got the
time?
2:00
TCP connection
response
<file>
TCP connection
request
Get http://www.awl.com/kurose-ross
computer protocols:

## Slide 15: Internet protocols
Communication between machines rather than humans
all communication activity governed by protocols
protocols define format, order of packets sent and received among network entities, and actions taken on packet transmission, receipt
TCP connection
response
<file>
TCP connection
request
Get http://www.awl.com/kurose-ross
computer protocols:
Notes: This course covers basic Internet protocols, enough for you to get a basic idea on how Internet works. Now how many protocols out there? A lot, group them together by layers

## Slide 16: Delivering data over the global Internet is a complicated process, involving many many steps
How to get the work done: divide and conquer
Group functions to a few modules
How many?
Notes: Dealing with complex systems: “Divide and conquer” principle. So each piece is manageable. Easier said than done. Hard problem? Is 7 a lucky #? Or 3 is better? How do people figure out the right number?

## Slide 17: Internet protocol stack
Application layer protocols
  Support data exchange between application processes
  Example: SMTP, HTTP, DNS
Transport layer protocols
  handling delivery reliability, multiplex within a host
  Example: TCP, UDP
Network layer protocols
  forward packets from source to destination
  Example: IP
Link layer protocols
  transfer data between directly connected network elements
  Example: Ethernet protocol, WiFi
Physical layer: bits “on the wire”
application
transport
network
link
physical
(Simple Mail Transfer Protocol)
Notes: At least some of the protocol stack runs on every node/element/box that is connected to the network
explicit structure allows identification, relationship of complex system’s pieces
  layered reference model for discussion
modularization eases maintenance, updating of system
  change of implementation of layer’s service transparent to rest of system
  e.g., change in gate procedure doesn’t affect rest of system

## Slide 18: Application View
Internet
These are application programs
They talk to each other using application protocols (web protocol: HTTP)
My Laptop -
Running web
browser
Web Server
www.cnn.com
client
server
(Chrome, Safari, Firefox, ...)
(Apache, GWS, ...)
Application protocols
Assume network can send data to any hosts on the Internet
Don’t know/care how data is sent, and assume all data delivered reliably
Runs on top of a transport protocol
apps
trans
net
link
phy
Notes: (process: running application)

## Slide 19: Transport View
Internet
A transport protocol's job: delivering data between the two communicating ends
  Don’t know or care about which paths data may traverse through the network
Multiple transport protocols exist, each offers somewhat different functions (e.g. reliability, congestion control)
My Laptop -
Running web
browser
client
Actually, transport protocols don’t do delivery  network protocol’s job
apps
trans
net
link
phy
Web Server
www.cnn.com
server
Notes: Transport protocol runs on end hosts

## Slide 20: Network Layer View
Internet
network protocol's job: forward packets from source to destination host
A really hard problem: the Internet is large, run by many different parties
  connection from laptop to CNN.com:
    WiFi  campus backbone  local ISP  other ISP  CNN website
ISP C
ISP A
ISP E
ISP B
“BIG COMPANY’s network”
apps
trans
net
link
phy
Notes: Because the Internet is huge!

## Slide 21: Link Layer View
Link layer’s job: Get a packet transmitted across some communication medium to next hop
Different medium  different link layer protocol
apps
trans
net
link
phy

## Slide 22: What protocol “layer” really means
Application
data
Application
protocol
Transport
protocol
Network
protocol
Link
layer
protocol
application
transport
network
link
physical

## Slide 23: (Tentative) Schedule of the Quarter
4
5
6
3
5
5
1
4
2
Mon
Wed
Week: 1 2 3 4 5
6 7 8 9 10
Mon
Wed
3/21: Final Exam
The big yellow numbers indicate the chapter numbers in the textbook.
Internet Protocol (IP)
Midterm
Addressing, NAT, IPv6
Routing in the Internet
Routing algorithms & protocols
Routing algorithms & protocols
Security 101
2
2
2
3
3
2/10 | 2/17 | 2/24 | 3/3 | 3/10
2/12 | 2/19 | 2/26 | 3/5 | 3/12 Course review
6
Link layer
(Ethernet)
Congestion Control
1/6 Course intro BW& delay | 1/13 HTTP | 1/20 Martin Luther King Jr. Day | 1/27 Transport protocols | 2/3
1/8 Socket programming, Web & HTTP | 1/15 DNS | 1/22 DNS | 1/29 TCP | 2/5
Hubs and switches
Presidents’ Day

## Slide 24: Packet Switching: Statistical Multiplexing
  Each node sends packets as soon as link available
  Receiver gets a full packet first, then forwards it towards the destination
Store-and-forward
Packet switch can temporarily buffer up packets
  Introduce delay
  Packets get dropped when the queue is full
Notes: Transport, Traffic system is by nature a packet switch
Freeway and Toll booth
Shared packet-by-packet on demand
Packet switching has all these problems, why is it even in the first place?
Every coin has 2 sides!

## Slide 25: Network Performance
3 basic measurements
  Throughput (bits/sec, Kbps=1000 bits/sec, Mbps)
  Loss rate (% of packets lost)
  Delay (sec, msec)
Throughput
  over a single link: point-to-point
    Pumping data into the pipe: throughput = link bandwidth
  Multi-access:
A
B
a lot more difficult to measure, Why?

## Slide 26: Packet Losses
Wired links
  Loss due to transmission errors
  Loss due to congestion
Wireless links
  Limited transmission rate
  Higher (than wire) bit error rate
  Host mobility: high variance in the number of hosts sharing the same wireless channel
Do users know there are packet losses?
Do users’ performance get affected by losses?

## Slide 27: Delay in packet-switched networks
4 sources of delay at each hop
node processing:
  check bit errors
  determine output link
Queuing
A
B
propagation
transmitting
nodal
processing
queueing
C
Transmission
  R = link bandwidth (bps)
  L = packet length (bits)
Propagation
  d = length of physical link
  s = propagation speed in medium (~2x108 m/sec)
= Length / rate
= distance/sec
= #packets in queue X transmission time of each packet

## Slide 28: Example: calculating one hop delay
total delay (AB) = ?
Queuing delay = ?
transmission delay = ?
Propagation delay = ?
Switch A
Switch B
link length = 100 km
Bandwidth= 1 Mbps
packet size= 1000 bits
(all pkts equal length)
(2.0x10^8 meters/sec in a fiber)

## Slide 29: Example: calculating one hop delay
total delay (AB) = ?
Queuing delay =
transmission delay =
Propagation delay =
Switch A
Switch B
link length = 100 km
Bandwidth= 1 Mbps
packet size= 1000 bits
(all pkts equal length)
(2.0x10^8 meters/sec in a fiber)
0.5 msec
1 msec
Waiting time for 2 pkts

## Slide 30: Transmission vs. propagation delay
bandwidth
time
1Mbps
1000 bits to send
0.5ms
1ms
Propagation: d / s
  d = length of a physical link
  s = signal’s propagation speed in the medium (~2x108 meter/sec)
Transmission delay: L / R
R = link bandwidth (bit-per-second, bps)
L = packet length (bits)
2Mbps
(2) =0.5msec
How long it takes to pump 1K bits into each pipe:
(1) =1msec
Notes: Notice: when the last bit is sent, where is the packet? At neither end
It’s in the pipe!

## Slide 31: Packet-switching: store-and-forward
Takes L/R seconds to transmit (push out) packet of L bits on to link of R bps
Entire packet must arrive at router before it can be transmitted on next link: store and forward
Example 1: send A  B
L = 8000 bits (1000 bytes)
Bandwidth R = 2 Mbps
If ignore propagation delay:
  delay = 3xL/R = 12 msec
R
R
R
L
A
B
L
i.e. when last bit of a packet left A, it arrives at router-1 instantly
router-1
router-2

## Slide 32: Packet-switching: store-and-forward
Example 2:
A sends 5 packets to B
L = 8000 bits, R = 2 Mbps
  Ignore propagation delay
How long does it take starting from A sending the first bit of first packet till B receives the last bit of the last packet?
R
R
R
time
T=0
1
L/R
2L/R
1
3L/R
1
2
2
3
3
2
1
3
2
3
4
4L/R
1
2
3
4
5L/R
5
1
2
3
5
4
6L/R
5
1
2
3
4
7L/R
1
2
3
4
5
What if one takes into account the propagation delay?
router-1
router-2

## Slide 33: Lets try an example
L = 4000 bits, R = 2 Mbps, A sends 4 packets
  L/R = 2msec, L/2R = 1ms
Propagation delay: 2msec for each link
When will first packet get to S2?
  A⇨S1: L/R + Dpropagation = 2ms+2ms
  S1⇨S2: L/2R + Dpropagation =
R
2R
R
L
A
B
S1
S2
S1
S2
L
L
L
1ms+2ms
T=5ms
T=6ms
When 1st packet arrives at S2, where is the 2nd packet?

## Slide 34: Lets try an example
L/R = 2msec, L/2R = 1ms
Propagation delay: 2msec for each link
When 1st packet arrives at S2, where exactly is the 2nd one?
R
2R
R
L
A
B
S1
S2
S1
S2
L
L
L1
L2
T=7ms
T=4ms: last bit leaves A
T=6ms: last bit arrives S1
T=7ms: last bit leaves S1
Notes: Ask: what if S1-S2 link is r/2, instead of 2R?

## Slide 35: Network latency
The time to send 1 packet from host A to B
  sum of delays across each hop along the path
RTT: round-trip-time
1
4
5
3
2
A
B
Notes: Note: (1) E2E total 5 nodes, 4 links in between, 3 switches
Assuming negligible delay at host B to turn around
Emphasize this is for one packet; what if A sends B 5 packets, what would be the total delay?

## Slide 36: What we covered today
Internet: made of a huge number of hosts, routers, wired and wireless links
Hosts: run application protocols to exchange data packets with each other
Routers: run bunch of protocols to move all packets towards their destinations
Why protocols are layered
How to calculate packet delays as they move across a packet-switched network

## Slide 37: Lecture 1 Review: layered protocol architecture

## Slide 38
Concepts:
  Internet: made of a huge number of hosts and routers, interconnected by physical and wireless links
  Host: a computer running applications and bunch of protocols to let apps exchange data with each other
  Router: a packet switch running bunch of protocols to move packets toward their destinations
Protocols are organized in layers:
  Application protocols
  Transport protocols
  Network protocols
  Link layer protocols
  Physical layer
How to calculate packet delays as they move across one hop
Notes: Today: first finish the discussion on delay calculation, then move on to socket programming

## Slide 39: Application protocol’s view of the world
HTTP
TCP/UDP
IP
Ethernet
interface
HTTP
TCP/UDP
IP
wireless
interface
IP
IP
Ethernet
interface
Ethernet
interface
SONET
interface
SONET
interface
host
host
router
router
HTTP message exchange
TCP segment delivery
IP packet
IP packet
IP packet
Ethernet frame
Access point (AP)
a reliable pipe
Web browser and server exchange formatted HTTP messages over a reliable pipe
As an application protocol, HTTP only concerns with the message’s presentation format
Application decides where msgs should be delivered to
  The receiving end is identified by its name, which gets translated to IP address

## Slide 40: Transport protocol’s view of the world
HTTP
TCP/UDP
IP
Ethernet
interface
HTTP
TCP/UDP
IP
wireless
interface
IP
IP
Ethernet
interface
Ethernet
interface
SONET
interface
SONET
interface
host
host
router
router
TCP segment delivery
IP packet
IP packet
IP packet
Ethernet frame
Access point (AP)
A transport protocol receives data blobs from an application process, delivers them to the destination process (reliably)
  Dest. Process is identified by IP address + (trans)port number
It runs between two processes over an unreliable network (where packets can be garbled, lost, or reordered)
apps
apps
unreliable packet delivery

## Slide 41: Network protocol’s view of the world
HTTP
TCP/UDP
IP
Ethernet
interface
HTTP
TCP/UDP
IP
wireless
interface
IP
IP
Ethernet
interface
Ethernet
interface
SONET
interface
SONET
interface
host
host
router
router
IP packet
IP packet
IP packet
Ethernet frame
Access point (AP)
data producer/receiver
data producer/receiver
Network protocol, IP, sees all IP-speaking nodes
It receives data segments, delivers each of them to its destination IP address (with its best effort)
  A router forwards packets, without looking inside IP envelope

## Slide 42: Link layer protocol’s view of the world
HTTP
TCP/UDP
IP
Ethernet
interface
HTTP
TCP/UDP
IP
wireless
interface
IP
IP
Ethernet
interface
Ethernet
interface
fiber
interface
fiber
interface
host
host
router
router
HTTP message exchange
TCP segment delivery
IP packet
IP packet
IP packet
Ethernet frame
Access point (AP)
A link layer protocol delivers data frames between two physically connected nodes
  A link-layer header is added at sending node, removed by the receiving node
  When a packet moves through the network across multiple hops: link-layer header is added and removed multiple times

## Slide 43: Layered protocol implementation
protocol header: contains the information one writes on the “envelope”
all the information, and only the information, that’s needed to carry out the protocol’s functionality
IP packet
IP hdr
DATA
TCP segment
TCP hdr
DATA
DATA
App protocol header
Ethernet frame
header
tail
DATA
not all link protocols have tail

## Slide 44: One more question: why 5 layers?
Two layers are taken as given
  Multiple different application protocols
  Multiple different physical communication media types
IP: the span layer
  Connecting up all nodes
Link layer: adaptation between IP and physical media
Transport: adaptation between what apps want and what IP offers
Application protocols
(HTTP, SMTP, FTP...)
IP
Communication media
Wireless, fiber, satellite. ...
transport layer
link layer
5-year protocol stack
Notes: Session = transport connection; presentation: handled by app protocol; YANG, DANIEL

## Slide 45: Network applications: how different parties reach each other

## Slide 46: Some popular network applications
Email
Web
WhatsApp
BitTorrent (P2P file sharing)
Online Games
YouTube
Virtual Conferencing
application
transport
network
data link
physical
application
transport
network
data link
physical
application
transport
network
data link
physical
Application processes communicate with each other using application protocols
Notes: How do they communicate? Who contact whom first?

## Slide 47: Client-server application communication model
servers:
Reachable by IP address
always-on, waiting for incoming requests from clients
clients:
Initiate communication with server
client/server
Q: How does a client process identify the server process with which it wants to communicate?
A: Using port numbers via the socket API (Application Program Interface)
Notes: Client: who send the first packet. Do/can clients talk to each other?
Exactly how you initiate, or how you wait?

## Slide 48
Serving multiple applications
socket
Operating system
(Mac OS, Linux,
windows, etc)

## Slide 49: Socket
Process: program running on a host
Between different hosts: Processes communicate through an application-layer protocol
process
TCP with
buffers,
variables
socket
host or
server
process
TCP with
buffers,
variables
socket
host or
server
Internet
Controlled
by Operating System
written by
app developer
A process sends/ receives messages to/from its socket
A socket analogous to a door:
  sending process shoves message out of the door
  transport protocol brings message up to the socket at receiving process

## Slide 50: What is "socket"
A set of system function calls
socket ( ): Create a socket
bind( ): bind a socket to a local IP address and port #
connect( ): initiating connection to another socket
listen( ): passively waiting for connections
accept( ): accept a new connection
Write( ): write data to a socket
Read( ): read data from a socket
Close( )
process
TCP with
buffers,
variables
socket
host or
server

## Slide 51: What is "socket"

## Slide 52: Socket: analogous to a door
client computer
server computer
socket( ): create a “door”
bind( ): tie the door to a [local IP addr, port#] pair
connect()
listen( ): start waiting for incoming packet with matching destination port#
2
4
3
4
6
8
6
11
close(): delete/remove a door
A couple other questions:
What is the server’s IP address?
  Website name  IP address
What port number to use?
  Client: assigned by OS
  Server: defined standards
28
131.179.128.19
216.58.219.46
77
Notes: accept( ): accept a new connection
Write( ): write data to a socket
Read( ): read data from a socket

## Slide 53: A quick comment about "port"
Web, Email, FTP all connect client to server by TCP
The server tells which client wants which service by well-defined port number:
  Web: port 80, ftp 21, mail 25
A server for email, web, ftp
Web request
Email request
FTP request
ftp:waiting for packets to port21
email process: port25
Web server: port80

## Slide 54: IP address, TCP connection, port number, processes, and sockets
web browser
process
12.2.3.4
Operating system
(including TCP, IP)
email server
process
port=25
web server
process
port=80
IP address: 131.179.128.19
port=2345
Apple Mail
process
Port=4567
18.2.3.4
Notes: Port numbers: below 1024 are controlled by IANA, Internet Assigned Numbers Authority
Individual user processes are assigned port numbers when creating a socket

## Slide 55: Applications
So far we’ve talked
Application process (executing application program)
Application protocol (used by application processes to exchange data)
Exactly how data is exchanged
  Socket
  Transport protocol
Lets look at exactly what data is exchanged
process
TCP with
buffers,
variables
socket
Notes: Sink into the hole of socket, then transport carries the data to the other end

## Slide 56: Web and HTTP
Web page: normally consists of
  base HTML-file, which includes
  several referenced objects
An object can be another HTML file, JPEG image, Java applet, audio file,…
Each object is addressable by a URL (Universal Resource Locator )
http://www.someschool.edu:port#/someDept/pic.gif
host name
path name
Application protocol
Notes: Port# is optional; use default if absent; explain 2 slides down
Path name:directory+file name

## Slide 57: What protocol “layer” really means
Application
data
Application
protocol
Transport
protocol
Network
protocol
Link
layer
protocol
application
transport
network
link
physical

## Slide 58: Acknowledgment
Slides adapted from S24 CS118 instructed by Prof. Lixia Zhang